## Slide 1: Characterizing Turbulence at a Prospective Tidal Energy Site: Observational Data Analysis
Katherine McCaffrey
PhD Candidate, Fox-Kemper Research Group
Department of Atmospheric and Oceanic Sciences
Cooperative Institute for Research in Environmental Sciences
Thank you to my advisor and collaborators:
Baylor Fox-Kemper, Dept. of Geological Sciences, Brown University, CIRES
Peter Hamlington, Dept. of Mechanical Engineering, CU Boulder
Jim Thomson, Applied Physical Laboratory, Univ. of Washington

## Slide 2: Outline
Introduction to Tidal Energy
Introduction to the Problem
Anisotropy, Coherence, and Intermittency
  Observations and Metrics
  Parameterization Results
Preliminary Statistical Model Results
Notes: Model results if there’s time

## Slide 3: Tidal Energy Resource
Clean, renewable, predictable energy source; close to population centers
DOE Resource Assessment: potential 250 TWh/year electricity generation (~6% of US usage)
http://www.tidalstreampower.gatech.edu/
Notes: Only 6% of total, but that can be concentrated where the people are

## Slide 4: Tidal Energy Conversion Technology
Barrages - use pressure differences on either side of a dam
In-Stream Turbine – in the flow, invisible from surface
http://www.infoniac.com/environment/world-s-biggest-tidal-turbine-to-be-built-in-scotland.html
http://www.darvill.clara.net/altenerg/tidal.htm
http://www.theecologist.org/News/news_analysis/67808how_france_eclipsed_the_uk_with_brittany_tidal_success_story.html
Rance, France – first and largest tidal barrage in the world: 240 MW
Notes: Barrages change tidal cycle and cause transportation issues – bad for tidal ecosystem
In stream – can’t SEE, but ships aren’t affected, ecosystem isn’t changed (at least not nearly as much as barrage… still area of research)

## Slide 5: Where are we now?
Bay of Fundy – successes and setbacks
European Marine Energy Centre, Orkney, Scotland test center
Thorough site characterizations at Admiralty Inlet and Nodule Point, Puget Sound, WA
Notes: Bay of Fundy – turbine plan 18 months, out after 6. Too strong, too turbulent… UNEXPECTED conditions
Highlights need for test sites for turbines as well as more thorough site characterization prior to installment

## Slide 6: Learning from Wind
Turbulence effects on power production: turbulence intensity
Turbulence effects on turbine mechanics (loads and subsequent gear box failures): coherent turbulent kinetic energy
Kaiser et al 2007
Kelley et al 2005
Wind speed
Power
Red – CTKE
Blue – Dynamic Pressure
Time (seconds)
Local Relative Energy Flux
Local Dynamic Pressure Response
Local CTKE Excitation
Notes: It is hard to gather many observations in the water, to know what even needs to be measured, so we learn from the wind industry what the important parameters are:
Turbulence intensity’s known effect no power production. EXPLAIN POWER CURVE.
Coherent turbulent kinetic energy’s effect on turbine loads (shown here are dynamic pressure and relative energy flux. EXPLAIN WAVELET MAP.

## Slide 7: Goals
Take the knowledge and experiences of the wind energy industry to further the development of tidal energy, focusing on turbulence.
Do a thorough physical description of the turbulence that will affect a tidal turbine
  Site classification for decision-making
  Describe realistic turbulence with metrics that can be used to improve models
    Turbulent in-flow generators: National Renewable Energy Laboratory’s TurbSim/pyTurbSim
    Tidal Array scale: ROMS
    Turbine scale: LES

## Slide 8: Nodule Point, Puget Sound, WA
Latitude | N 48 01.924’
Longitude | W 122 39.689’
Depth | 22m
Dates | Feb 17-21, 2011
Sampling Frequency | 32 Hz
Noise | 0.02 m/s
Proposed Hub Height | 4.7m
Hub Height Max. Velocity | 1.8 m/s
Thomson et al, 2012
Notes: Two observational campaigns
Describe ADCP – can’t calculate higher order statistics because of the inherent noise from beam spread.
Describe ADV – higher resolution, but only one height.
Velocities at NP: max of 1.8 m/s, 0.8 m/s slack tides shown.

## Slide 9: Turbulence Metrics
Turbulence Intensity:
Coherent Turbulent Kinetic Energy:
Mean u (m/s)
Iu (%)
StDev u (m/s)
Notes: Iu is purely statistical, and therefore saying nothing about the physical turbulence
CTKE is instantaneous – not REALLY “coherent” but it does get closer to the correlations through the cross terms of the Reynolds Stresses

## Slide 10: Turbulence Metrics
Anisotropy Tensor
Invariants:
CTKE-like, but built from invariants: Anisotropy Magnitude
  Independent of chosen coordinate system
All real flows fall somewhere in this triangle
Three component limit
One component limit
Two component limit
Notes: CTKE and Iu change depending on chosen principle axes
Use metric well-founded in turbulence theory, and the invariants that are universal.
Lumley Triangle has physical description of 1, 2 and 3 comp turbulence

## Slide 11: Physical Turbulence
What physical features are there to turbulence?
  Size – how big? The size of the turbine? Larger? Smaller?
  Frequency – how often do these “events” happen?
  Shape – flat, pancake-like? 3-d
How do we measure these?
  Coherence – how long is the flow correlated?
  Intermittency – how “random” is the flow?
  Anisotropy – how many velocity components contribute to the fluctuating velocity?

## Slide 12: Coherence
Temporal Autocorrelation
  Integral Scale
  Taylor Scale
τ (seconds)
R(τ) (%)
Λ=10.13 sec
λ=0.08 sec
Notes: Integral scale – how long is it correlated?
Taylor scale – how long until it’s no longer correlated?

## Slide 13: Intermittency
Intermittency manifests itself in departures from a normal distribution in the probability density function of velocity differences.
Pdfs of the velocity perturbation differences, ∆u’ (circles), ∆v’ (squares), and ∆w’ (diamonds), with Gaussian curves for reference (dashed). Black shapes have a time step of ∆t = 1 (~3 cm), gray are ∆t = 115 (~3 m), and white are ∆t = 230 (~6 m).
Higher order moments support the lack of Gaussianity in the pdfs.
Mean
Kurtosis
Skewness
Standard Deviation
Δu/σ
Probability

## Slide 14: Anisotropy
Improvement to the anisotropy analysis: For eigenvalues, λi, of the anisotropy tensor, aij, ordered from greatest to least, the barycentric coordinates are defined by:
Banerjee et al 2007
C1c : one-component limit –
linear
C2c : two-component limit –
planar
C3c : three-component limit –
isotropic
Three component limit
Two component limit
One component limit

## Slide 15: Parameterization
How do we represent how “turbulent” a location is?
  Often turbulence intensity is all that is used
  What about intermittency, coherence, and anisotropy?
Mean u (m/s)
Iu (%)
A (m2/s2)
A (m2/s2)
CTKE (m2/s2)
Notes: Mean u doesn’t tell us everything for Iu…. What about A? Color by A add information about the anisotropy. Not directly correlated with Iu,
A was made to be like CTKE, and they are closely correlated, so use A instead of CTKE.

## Slide 16: Parameterization: Shape
Iu only measures one component (u)
A (m2/s2)
The highest instance of each parameter (large shapes) is close(r) to the one-component limit.
Iu (%)
CTKE (m2/s2)
A is better than CTKE
Three
One
Two
Notes: Big shapes are the highest for each parameter – notice they’re closer to 1 comp.
CTKE is completely scattered.
Iu only measures one component by definition, so it is skewed.
A is better then CTKE.
REMAKE THESE FIGURES!!!!!!!!!!!!!

## Slide 17: Parameterization: Size
 | λ | Λ
Iu | 0.596 | 0.450
CTKE | 0.680 | 0.017
A | 0.884 | 0.317
The anisotropy magnitude, A, captures the the behavior of CTKE (and therefore loads?), intermittency in the pdf, the shape from the barycentric map, and the coherence of the correlation function.
A (m2/s2)
λ (seconds)

## Slide 18: Conclusions
A new, tensor-invariant metric for physically describing turbulence, the anisotropy magnitude, is introduced
Turbulence intensity does not parameterize intermittency, coherence, or anisotropy as well as other easy-to-measure metrics such as CTKE and A.
The anisotropy magnitude does the best job at representing intermittency, coherence, and anisotropy.
If A is similar to CTKE, does it have the same strong correlation to turbine loads?
How well does the coherence function in pyTurbSim represent the observations in terms of A?

## Slide 19: Next step…
  The NREL pyTurbSim model (Jonkman & Kilcher) creates stochastic turbulence.
  The NCAR LES model (Sullivan et al.) includes more realistic ocean physics.
J. Jonkman, L. Kilcher, TurbSim user’s guide: Version 1.06. 00, Golden, CO: National Renewable Energy Laboratory (2012).
P. P. Sullivan, J. C. McWilliams, C.-H. Moeng, A subgrid-scale model for large-eddy simulation of planetary boundary-layer flows, Boundary Layer Meteorology 71 (1994) 247–276.
  How well do the models do at generating realistic turbulence?
  How do the statistics calculated from the model output compare to those from the observations?

## Slide 20: Introduction to pyTurbSim
Stochastic turbulence generator
  Inputs:
    Background mean flow profile
    Spectral density curve
    Turbulence intensity and Reynolds stresses
  Method:
    Inverse fast Fourier transform
    Optional additional spatial coherence function
  Outputs:
    Three-component velocity time series
Model Input | 
Latitude | 48N
Depth (RefHt) | 22m
Uref | 1.8 m/s
Sampling Frequency (timestep) | 10 Hz
Hub Height | 4.7m
___________________ u’w’ | .0011 m2/s2
__________________ u’v’ | .0009 m2/s2
_____________________ v’w’ | .0004 m2/s2
Turb Model | TIDAL
Profile Type | H2L (log)

## Slide 22: Preliminary Results
Baseline statistics, before coherence is added
A (m2/s2)
Iu (%)
CTKE (m2/s2)
CTKE (m2/s2)
A (m2/s2)

## Slide 23: Thank you!
Stay tuned for model results at the Boulder Fluid Seminar December 10th!